## Slide 1: TileSR: Accelerate On-Device Super-Resolution with Parallel Offloading in Tile Granularity
Ning Chen, Sheng Zhang, Yu Liang, Jie Wu, Yu Chen, Yuting Yan, Zhuzhong Qian and Sanglu Lu
Notes: Hello, everyone, my name is Ning Chen, from Nanjing University. Today I will introduce the paper titled “TileSR: Accelerate On-Device Super-Resolution with Parallel Offloading in Tile Granularity”

## Slide 2: Outline
Problem Background
  Edge Collaborative SR with Parallel Offloading
    Key steps: image dividing, tile-based offloading
  Challenges
    SR difficulty, device priori information
Related Works
Motivations
System Model
  TileSR: Parallel Offloading Tiles to Accelerate Inference
Experiments
Notes: Here is the outline, I will first introduce the problem background, and simplify the related works. Then, based on the key observations, we propose our system TileSR, which uses parallel offloading to accelerate image super resolution. Finally, we do lots of experiments to evaluate the system performance.

## Slide 3: Background: Single-Device SR
On-device video super-resolution
  Unreliable network leads to low-quality video
  Local SR to enhance the video quality
CDNs
User
Media server
360P
720P
360P
1080P
1080P
1080P
Notes: Let's start with the background. We often watch some live videos in the internet, however, because the unreliable network in the downstream, the video we received can hardly maintain the high-quality for a long time. A nature idea is to perform local super-resolution to enhance the video quality.

## Slide 4: Background: Single-Device SR
On-device video super-resolution
Challenges: local resource constrained
  Computation  long inference delay
  Memory  hard to store intermediate data
  Energy  hard to support long-term inference
SR model | 270p (s) | 360p (s) | 540p (s) | 720p (s)
MSRN X2 | 0.075 | 0.167 | 0.302 | 0.922
MSRN X3 | 0.083 | 0.182 | 0.321 | 1.003
MSRN X4 | 0.091 | 0.237 | 0.404 | 1.118
RCAN X2 | 0.269 | 0.595 | 1.057 | 3.191
RCAN X3 | 0.277 | 0.610 | 1.085 | 3.261
RCAN X4 | 0.287 | 0.632 | 1.149 | 3.356
Notes: However, on-device super-resolution poses significant challenges as the local resources are constrained. For example, the limited computation leads to long inference delay, the limited memory can hardly to store the intermediate data, and the limited energy cannot support long-term CNN inference.

## Slide 5: Background: Multi-Device SR
Multi-device inference for image/video SR
  Model downloading from cloud
SR Model Zoo
Cloud
Access Point
Local Device
Device 1
Device 2
Device 3
Model Update
Base Station
Notes: In such dilemma, multi-device collaboration for video super-resolution is proposed. It contains two key steps: firstly, each device downloads the proper SR models from remote cloud

## Slide 6: Background: Multi-Device SR
Multi-device inference for image/video SR
  Model downloading from cloud
  Image dividing  multiple tiles
SR Model Zoo
Cloud
Access Point
Local Device
Device 1
Device 2
Device 3
Model Update
Base Station
Images
Tiles
Notes: Then, the local device partitions the incoming image into multiple tiles,

## Slide 7: Background: Multi-Device SR
Multi-device collaboration for image/video SR
  Model downloading from cloud
  Image dividing  multiple tiles
  Parallel offloading  tile inference
SR Model Zoo
Cloud
Access Point
Local Device
Device 1
Device 2
Device 3
Model Update
Tile Offloading
Base Station
Images
Tiles
Notes: and offloads the tiles to the collaborative devices. Finally, the collaborative devices returns the SR results to the local devices

## Slide 8: Background: Multi-Device SR
Multi-device collaboration for image/video SR
Challenges
  How to divide? even or uneven?
  How to offload? without prior offload reward
Notes: This collaborative framework faces two key challenges. Firstly, how to divide the images, even dividing or uneven dividing? Second, without the prior knowledge, such as the system-side information of each device. Next, I introduce two previous works.

## Slide 9: Related Works
Supremo TMC 2022
  Layer: edge-cloud collaboration
  Methods: based on the “edge” feature
Notes: The first work is Supremo, which uses edge-cloud collaboration rather than multi-edge device to run CNN super-resolution. It first divides the image into multiple tiles based on the image “edge” feature, then, it offloads the tiles with more edges to cloud for CNN inference, but do interpolation for the remaining tiles. Thought it uses residual encoding to reduce the data volume, the cloud-assisted method incurs large transmission delay.

## Slide 10: Related Works
MobiSR MobiCom 2019
  Methods: dispatch images to diverse processors
Notes: The second work is MobiSR, it does not have the image dividing process, it dispatches the incoming images to diverse processors, such as CPU, GPU and DSP. However, the CPU capacity in common mobile device is so weak that it incurs long inference delay, thereby hardly meeting the requirement of real-time.

## Slide 11: Motivation: Difficulty Analysis
Visual structural complexity
  Utilize two methods, interpolation and CNN-based
    Higher structure, higher upscale quality (PSNR)
    Higher structure, it benefits less from CNN inference
How to measure the structure information?
Notes: To make efficient image dividing and tile offloading , we first discuss the relationship between super-resolution difficulty and the enhanced quality. We first consider the visual structural complexity. For two images, image a is structured and image b is unstructured, we use interpolation-based and CNN-based method to upscale them. We find that higher structure leads to high upscale quality, but compared lower structure, it benefits less from CNN inference. Now, we transform the problem to measure the structure information.

## Slide 12: Motivation: Difficulty Analysis
Pixel Variant Matrix for image ,
Mean Pixel Variant
  This definition applies to tile as well
Notes: Hence, we next analysis the relationship between the pixel feature and the SR difficulty. Specifically, we define the pixel variant matrix PV_f for image f, and each item represent the summed pixel variant with surrounding 8 pixel points.

## Slide 13: Motivation: Difficulty Analysis
Mean Pixel Variant
Motivative insights
  Tiles with low-mPV achieve high and similar PSNR using CNN-based and interpolation-based methods;
  Tiles with high-mPV get significant higher PSNR using CNN-based method than interpolation.
Dataset | DIV2K
Interpolation method | AREA_x2
CNN model | CARN_x2
Dividing method | 20 x 20

## Slide 14: Tiles Generation
Mean Pixel Variant
Key Idea: only offload high-mPV tiles
  Calculate the upscaling difficulties for each tile;
  Select the Top-K tiles with highest mPV;
  Parallel offload the selected tiles to involved devices for CNN-based inference;
  Locally upscale other tiles via interpolation.
Next we consider the parallel offloading policy!

## Slide 15: Parallel Offloading: System Model
Multi-device parallel offloading problem
  Decision:
  Maximize the overall offload reward
  Subject to the resource and latency constraints
No System-side info.
i.i.d random reward
Resource constraint
Latency constraint

## Slide 16: Parallel Offloading: System Model
Multi-device parallel offloading problem
  Decision:
  Proportional fairness maximization
No System-side info.
i.i.d random reward
Resource constraint
Latency constraint
Fair reward distribution

## Slide 17: Parallel Offloading: Algorithm
Reward is uncertain but bounded
  Decentralized multi-agent multi-armed bandit
    Exploration: obtain the offloading reward mapping
    Packing: get the final tile offloading scheme
    Exploitation: utilize the packing result

## Slide 18: Parallel Offloading: Algorithm
Reward Exploration and Exploitation
  Group-based offloading in a round-robin fashion
    Target device
    Reward update

## Slide 19: Parallel Offloading: Algorithm
Tile packing based on reward map
  For each slot , it can be modeled as
Value
Volume
Multi-Knapsack Problem (MKP)

## Slide 20: Parallel Offloading: Algorithm
Tile packing upon MKP
  Iteratively update the tiles for each device
Slove single-knapsack problem for device
Update the decision set
Update the profit matrix

## Slide 21: Parallel Offloading: Algorithm
Tile packing upon MKP
  Example: 4 tiles, 3 devices

## Slide 22: Experiments
Experimental setup
  Edge device and CNN models
  Datasets: DIV2K/Set5/Set13/YouTube-NBA

## Slide 23: Experiments
Experimental setup
  Edge device and CNN models
  Datasets: DIV2K/Set5/Set13/YouTube-NBA
  Comparing schemes
    Supremo: offloads tiles to cloud
    MobiSR: utilizes local multiple diverse processor
    Strawman: utilizes CARN for local SR
    RAScheduler: offloads tiles based the computation

## Slide 24: Experiments
Tradeoff between latency and quality
  Latency: 17.77%, 57.63%, 69.66%, and 82.2%
  SR quality: 2.38%, 9%, 3.2%, and 10.57%

## Slide 25: Experiments
Processing Rate (fps)
  0.22x, 1.36x, 2.3x, and 4.62x

## Slide 26: Experiments
Energy efficiency
  7.6%，40%，28%

## Slide 27: Experiments
Tile settings
  Tile quantity: 20；Tile size: 15x15

## Slide 28: Conclusion
Multi-device inference for image SR
  SR difficulty analysis
    Method: Top-K tiles are offloaded for CNN inference, others are executed locally.
  Tile parallel offloading
    Decentralized multi-agent multi-armed bandit
    Exploration: obtain the offloading reward map
    Packing (MKP): iteratively solve a single-knapsack problem for each device

## Slide 29: Thank You !
Q & A
Ning Chen
Nanjing University